## Slide 1: Chapter :-4 Network Layer

## Slide 2
Introduction
Network layer Duties:
Duties of network layer
Internetworking
Addressing
Routing
Packetizing
Fragmenting
Design Issues of Network Layer:
The important network layer design issues include the service provided to the transport layer and the internal design of subnet.
The network layer has been designed with the following goals:
The services provided should be independent of the underlying technology. Users of the service need not know about the physical implementation of the network.
This design goal has great importance because there is a great variety of networks in operations.
The design of the layer must not disable us from connecting to networks of different technologies.

## Slide 3
4. The transport layer should be shielded from the number, type and different topologies of the number of the subnets users uses. That is, all that the transport layer wants is a communication link, it need not know how that link is established.
5. Finally there is a need for some uniform addressing scheme for network addresses. With these goals in mind, two different types of services emerged:
Connection Oriented Network Services.
Connectionless Network Services.
STORE AND FORWARD PACKET SWTICHING:
1. Implementation of connectionless services: 2. Implementation of connection oriented services:

## Slide 4
Internal Organization of the Network Layer:
Basically there are two philosophies for organizing the subnet:
1. To use connection oriented service.
2. To use connectionless service.
In the connection oriented service, a connection is called as virtual circuit. It is similar to a physical connection between the sender host and the destination host.
In the connectionless organization the independent packets are called as datagrams. They are analogus to telegrams.
VIRTUAL CIRCUITS:
The principle behind the virtual circuits is to choose only one route from source to destination.
When connection is established, it is used for sending all the traffic over this connection.
When the connection is released, the virtual circuit is terminated.
Features:
Every router have to maintain and update a table.
Each packet must have a virtual circuit number field in its header in addition to sequence number checksum etc.
It is necessary to set up a VC before communication.
The users are charged for connect time as well as for the amount of data transported.

## Slide 5
DATAGRAM:
With a datagram, the routes from source to destination are not decided in advance.
Each packet sent is routed independently. Different packets of the same message can follow different routes.
The datagram subnets have to do more work but they are more robust and deal with failures and congestion more easily as compared to VC subnets.
Features:
The routers do not have to maintain any tables.
Each datagram must contain full destination address. The address can be very long.
When a packet comes in the router finds an available outgoing line and sends the packet out on that line. So that it can reach to the destination.
Comparison of virtual circuits and Datagram subnet
Delivery: The network layer supervises how the packet are being handled by the underlying physical networks. This handling is known as the delivery of packets.
The two different methods of delivery are:
Direct delivery.
Indirect delivery.

## Slide 6
Direct Delivery:
In the direct delivery the destination host and the one who delivers the packet are in same physical network.
The sender can extract the network address of the destination using the mask. If then compares this address with the addresses of the network to which it is connected. If these two address are identical then the delivery is direct.
HOST 1
HOST 2
Physical Network
MSG
MSG
Direct Delivery
Direct Delivery
To the rest of internet

## Slide 7
Indirect Delivery:
In the indirect delivery of packets, the sender host and the destination host are not the part of the same physical network.
In such a situation, the packet travel from one router to the other and are finally delivered to the destination host.
The indirect delivery involves one direct and zero or more indirect deliveries. The last delivery is always direct one
Physical Network
Physical Network
Sender
Destination
Indirect Delivery
direct Delivery
MSG
MSG

## Slide 8
Forwarding: It is defined as the process of placing the packet in its route towards its destination. Forwarding is possible only if the host or a router have a routing table of their own.
A sender host or a router will refer to this routing table when it receives a packet and from the table they will find the root to the final destination.
But this simple solution has practically become impossible today in the internetwork environment due to large number of entries required to be made in a routing table.
Forwarding Technique:
Many techniques have been invented and tested in order to make the size of the routing tables manageable. Some of them are as follows:
Next hop method versus route method.
Network specific method versus Host specific method.
Default method.
1. Next hop method versus route method:
The route method is the most basic method in which the information about the complete route is stored in the routing tables of hosts and routers. This makes the routing table extremely large and difficult to manage.
In order to reduce the size of routing tables, the next hope method is used in which the routing table contains only the address of the next hope instead of information about the complete route.

## Slide 9
2. Network Specific Method versus Host Specific Method:
In host specific method, the routing table of host or router will specify each destination host connected to the same physical network. This increases the number of entries in a routing table and makes it large.
But in the network specific method, we have only one entry corresponding to the destination network NB.
That means we consider all the host connected to the same network NB as one single entry. This will reduce the routing table and simplify the searching process considerably.
3. Default method:
This is one more method o simplifying the routing tables, in which host the sending host is connected to the network with two routers R1, R2.
Router 2 routes the packet to the hosts connected to network NB. However router R1 is used for the rest of the internet.
Hence in the routing table instead of listing all the networks in the entire Internet, host X will have only one entry called as the default entry.
sender
Network NA
Network NB
Rest of the internet
R2
R1
1
2
n
Default routing

## Slide 10
Routers:
Routers are devices that connect two or more networks. They consists of a combination of hardware and software.
The hardware can be in the form of a network server, a separate computer or a special device, as well as the physical interface to the various networks in the internetwork.
Various types of networks can be interconnected through routers.
The software in a router are the OS and the routing protocol. Management software can also be used.
Device A
Device B
Network
Network
Router
7
6
5
4
3
2
1
7
6
5
4
3
2
1
3
2
1

## Slide 11
Routers use logical and physical addressing to connect two or more logically separated networks.
The large network is organized into small network segments called as subnet and those subnets are interconnected via routers.
Each of the subnet is given a logical address. This allows the networks to be separated but still access each other and exchange data.
Data is grouped into packets, or blocks of data. Each packet has a physical device address as well as logical network address.
The network address allows routers to calculate the optimal path to a workstation or computer.
Route discovery is the process of finding the possible routes through the internetwork and then building routing tables to store that information. The two methods of route discovery are:
Distance vector routing.
Link state routing.
In distance vector routing, each router advertises its presence periodically to other routers on the network.
Link state routers broadcast their complete routing tables only at start-up and at certain intervals.
Dynamic route selection permits routers to constantly adjusting to changing network conditions.
With static route selection, packet always follow a pre-determine path.

## Slide 12
Routing Tables: The routing table for a host or a router consists of an entry for each destination, or a combination of destinations to route the IP packets.
Routing tables can be of two types:
Static routing tables.
Dynamic routing tables.
1.Static Routing Tables:
The information in the static routing tables is entered manual. The route of a packet to each destination is entered into the table by the administrator.
This routing table can not update itself automatically. It has to be changed manually as and when required.
Hence static routing table is useful only for small networks.
2. Dynamic Routing Table:
The dynamic routing tables can get automatically updated by using a dynamic routing protocol such as RIP, OSPF or BGB.
3. Unicast Routing:
In unicast routing there is a one to one relation between the source and the destination. That means only one source sends packets to only one direction.
The type of source and destination addresses included in the IP datagram are unicast addresses assigned to the hosts.
The concept of unicast routing when a router receive a packet, it forwards that packet through only one of its ports which corresponds to the optimum path.
The router can discard the packet if it can not find the destination address.

## Slide 13
Source A
Source B
Fig: Unicast Routing
Metric:
A metric is defined as the cost assigned for passing through a network.
The metric assigned to each network depends on the type of protocol

## Slide 14
Interior and Exterior Routing:
An internet is so large that for one routing protocol it is impossible to handle the tasks of updating the routing tables of all the routers.
So an internet id divided into a number of autonomous system(AS). An AS is group of networks and routers.
Interior Routing: The routing that takes place inside an AS is called interior routing.
Exterior Routing: The routing that takes place among various autonomous system is called exterior routing.
Broadcasting Routing: In certain application, the host has to send packets to many or all other hosts.
If the sender send a packet to all destination simultaneously then it is called as broadcasting.
Broadcasting
Simple Broadcasting
Flooding
Multidestination routing
Simple Broadcasting: In this method the source will simply send a distinct packet to each destination.
This method has two drawbacks:
A lot of bandwidth is wasted.
The source has to have a completed list of all destination.
2. Flooding: Flooding is another method used for broadcasting. The problem with flooding is that it has a point to point routing algorithm.
So it consumes a lot of bandwidth and generates too many packets.

## Slide 15
Multidestination Routing:
This is the third algorithm used for broadcasting.
In this algorithm each packet will contain a list of destination or a bit map which indicates the desired destination.
When each packet arrives at a router, the router first checks all destination. Then it decides the set of output lines that will required based on the destination address.
The router than generates a new copy of the received packet for each output line to be used. It includes a list of only those destination that are to use the line in each packet going out on that line. This will save bandwidth to a great extent. Also generation if too many packets right from the sending end will also be avoided.
Multicast Routing:
In multicasting a message from sender is to be sent to a group of destination but not all the destinations in a network.
A process has to send a message to all other processes in the group. For a small group it is possible to send a point-to-point message.
But this is expensive if the group is large. So we have to send messages to a well defined groups which are small compared to the network size.
Sending message to such a group is called multicasting and the routing algorithm used for multicasting is multicast routing.
Multicast routing is a special class of broadcast routing.

## Slide 16
Routing Algorithm:
One of the important function of the network layer is to route the packet from the source machine to the destination machine.
Routing algorithms is a part of network layer software. It is responsible for deciding the output line(port) over which a given packet is to be sent.
Such a decision is dependent on whether the subnet is a virtual circuit or it is datagram switching.
Desired Properties of a Routing Algorithm:
Optimality.
Fairness.
Robustness.
Stability.
Correctness.
Type of Routing Algorithm:
Non-adaptive (Static) Algorithm.
Adaptive(Dynamic) Algorithm.
1.Non-Adaptive Algorithm: For this type of algo, the routing decision is not based on the measurement or estimation of current traffic and topology. However the choice of the route is done in advance, offline and it is downloaded to the routers. So the choice of routing cannot be changed in this event of congestion or link failure. This is called non adaptive Algorithm.

## Slide 17
2. Adaptive Algorithm: For these algo, the routing decision can be changed dynamically if there are any changes in topology or traffic etc. This is called dynamic routing ot Adaptive Algorithm.
Optimality Principle:
It stated that if router J is on the optimal path from router I to router K, then the optimal path from J to K will also be along the same route.
Suppose route from I to J is r1 and rest of the route is called r2. If a route better than r2 is existed from J to K, it could be concentrated with r1 to improve the route from I to K so that r1r2 is optimal.
Sink Tree:
A set of optimal routes from all the source given destination form a tree called sink tree. The root of the sink tree is at destination.
A sink tree need not be unique. Other trees with the same path lengths may also exist.
All the routing algo are supposed to discover and use the sink tree for all routers.
In the sink tree the distance metric is the number of hops .

## Slide 18
b
a
c
j
i
e
d
g
h
f
d
f
a
b
c
j
i
e
g
h

## Slide 19
Static Algorithms:
Shortest Path routing.
Flooding.
Flow based routing
Shortest Path routing: This is based on simplest and most widely used principle. Here a graph of subnet is prepared in which each node represent either a host or a router and each arc represent a communication Link.
So as to choose a path between any two routers, this algo simply finds the shortest path between them.
How to decide the shortest path?
One way of measuring the path length is the number of hops. Another way is the geographical distance in KMS.
Some other metrics are also possible. For example we can label each arc with the mean queuing and transmission delay and obtain the shortest path as the faster path.
Labels on the ARC:
The labels on arc can be computed as a function of distance bandwidth, average traffic, mean queue length, cost of communication, measured delay etc.
The algo compares various parameters and calculate the shortest path, on the basis of anyone or combination of criteria mention above.

## Slide 20
2. Flooding: In this algo, every incoming packet is sent out on every outgoing line except the line on which it is arrived. That is why the name flooding. Each line except the incoming line are flooded with the copies of the same packet.
One disadvantage of flooding is that it generate a large no of duplicate packets. In fact it produce finite no of duplicate packets unless we somehow stop the process.
There are various damping technique:
Using a hop counter
To keep track of which packet have been flooded.
Selective flooding.
To prevent endless copies of packet circulating for a very long time through network a hop count may be used to suppress onwards transmission of packets after a no of hops which exceed the network diameter.
Flooding has two interesting characterstics that rise from the fact that all possible routes are tried:
As long as there is a route frm source to destination the packet wil be definitely delivered to the destination.
One copy of the packet will reach the destination via quickest possible route.
Selective Flooding: This is slightly more practical type of flooding principle. In this algo, every incoming packet is not sent out on every output line. Instead packet is sent only on those line which are likely to go in desired direction.

## Slide 21
Applications:
Flooding does not have many practical application, but it is useful in military application where a large no of routers are blown into pieces at any instant. So placing a packet on every outgoing line really makes sense.
In such application robustness of flooding is very much desirable.
Second application is in the distributed database application.
Flooding always chooses the shortest path so it produce the shortest possible delay.

## Slide 22
Dynamic Routing Algorithms:
The modern computer networks normally use the dynamic routing algorithm.
Two dynamic routing algorithm namely distance vector routing and link state routing are used popularly.
Both these algorithm are suitable for the packet switched networks.
Both these algorithms assumes that a router knows the address of each neighbouring router and the cost of reaching each neighbour.
In the distance vector routing, each node tells its neighbours about its distance to every other node in the network.
In the link state routing, a node tells every other node in the network the distance to its neighbour.
So both these routing algorithm are distributed type and so they are suitable for large internetworks.
In this algorithm, each router maintains a table called vector, such a table gives the best known distance to each destination and the information about which line to be used to reach there.
This algorithm is sometimes called by other names such as:
Distributed Bellman-Ford routing algorithm.
Ford-Fulkerson algorithm.
In distance vector routing, each router maintains a routing table. It contains one entry for each router in the subnet.
This entry has two parts:
The first path shows the preferred outing line to be used to reach the specific destination and
Second part gives an estimate of the time or distance to that destination.
Distance Vector: In distance vector routing, we assume that each router knowns the identity of every other router in the network, but the shortest part of each router is not known.
A distance vector is defined as the list of <destination, cost> tuples, one tuple per destination. Each router maintains a distance vector.
The cost in each tuple is equal the sum of costs on the shortest path to the destination.