## Slide 1
Prof. Krunal D. Vyas
9601901005
krunal.vyas@darshan.ac.in
3130704
Digital Fundamentals
Module 1:
Fundamentals of Digital Systems and Logic families

## Slide 2: Topics to be covered
Logic Gates
Boolean Algebra
Number Systems
Codes
Logic Family Terminology

## Slide 3: Logic Gates
Most basic logical unit of the digital system is gate circuit
Types of gate circuits are as follows
  AND Gate
  OR Gate
  NOT Gate (Inverter)
  NOR Gate
  NAND Gate
  XOR Gate
  XNOR Gate

## Slide 4: 1. AND Gate
AND Gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when ALL of its inputs are at logic level “1”
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input AND Gate

## Slide 5: 2. OR Gate
OR Gate or Inclusive-OR gate has an output which is normally at logic level “0” and only goes “HIGH” to a logic level “1” when one or more of its inputs are at logic level “1”.
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table
2-input OR Gate

## Slide 6: 3. NOT (Inverter) Gate
NOT gate has an output which is always opposite to input level.
A
C
Logic Notation
A | C
0 | 1
1 | 0
Truth Table
Inverter Gate

## Slide 7: 4. NOR Gate
NOR Gate is an OR gate followed by an inverter.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Truth Table
2-input NOR Gate

## Slide 8: 5. NAND Gate
NAND Gate is an AND gate followed by an inverter.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table
2-input NAND Gate

## Slide 9: 6. Exclusive-OR (X-OR) Gate
X-OR gate that has 1 state when one and only one of its two inputs assumes a logic 1 state and has 0 state when all of its input are same.
Also known as anti-coincidence gate or inequality detector.
A
B
C
Logic Notation
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table
2-input XOR Gate

## Slide 10: 7. Exclusive-NOR (X-NOR) Gate
X-NOR gate that has 1 state when all of its input are same and has 0 state when one of its input has 0 state and other input is 1 state.
Also known as equality detector.
A
B
C
Logic Notation
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
2-input XNOR Gate

## Slide 11: NAND as Universal Gate
NOT using NAND
A
A’
A
B
(AB)’
((AB)’)’ = AB
AND using NAND
A
B
A’
(A’B’)’ = (A+B)
OR using NAND
B’

## Slide 12: NOR as Universal Gate
NOT using NOR
A
A’
A
B
(A+B)’
((A+B)’)’ = A+B
OR using NOR
A
B
A’
(A’+B’)’ = AB
AND using NOR
B’

## Slide 13: Boolean Algebra
AND laws
OR laws
Commutative laws
``

## Slide 14: Boolean Algebra
Distributive laws
Redundant Literal Rule
Idempotent laws
Absorption laws

## Slide 15: Boolean Algebra
De Morgan’s Theorem
Break the line change the sign

## Slide 16: Proof of
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
A+B+C
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
From truth table, it is clearly visible that L.H.S. = R.H.S. Hence, the complement of a sum of variables is equal to the product of their individual complements.
L.H.S.
R.H.S.

## Slide 17: Proof of
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
ABC
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
1
1
1
1
0
0
0
0
1
1
1
1
0
0
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
From truth table, it is clearly visible that L.H.S. = R.H.S. Hence, the complement of a product of variables is equal to the sum of their individual complements.
L.H.S.
R.H.S.

## Slide 18: Reducing Boolean Expression
Reduce the expression
(Distributive law)
(Distributive law)
(A.A = A)
(1 + A = 1)

## Slide 19: Reducing Boolean Expression
Reduce the expression
(DeMorgan’s law)
(DeMorgan’s law)
(Distributive law)
(Distributive law)
(A.A’ = 0)
(Distributive law)
(A.A’ = 0)

## Slide 20: Exercise
Show that

## Slide 21: Number Systems
Unit – 1: Binary Systems & Logic Circuits Darshan Institute of Engineering & Technology

## Slide 22: Common Number Systems
System | Base | Symbols | Used by Humans? | Used in Computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 23: Quantities / Counting
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 24: Conversion among Bases
Possibilities
Example
Hexadecimal
Decimal
Octal
Binary
2510 = 110012 = 318 = 1916
Base

## Slide 25: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1 and so on
Decimal
Binary

## Slide 26: Example (Decimal to Binary)
12510 = ?2
2
125
1
2
62
0
2
31
1
2
15
1
2
7
1
2
3
1
2
1
1
0
12510 =
11111012

## Slide 27: Example (Decimal to Binary)
0.687510 = ?2
0.6875 x 2 =
1.3750
1
0.3750
+
0.3750 x 2 =
0.7500
0
0.7500
+
0.7500 x 2 =
1.5000
1
0.5000
+
0.5000 x 2 =
1.0000
1
0.0000
+
0.687510 =
0.10112
integer
fraction

## Slide 28: Exercise
(32)10 = ( )2
(555)10 = ( )2
(12999)10 = ( )2
(157.63)10 = ( )2
(64.125)10 = ( )2

## Slide 29: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Binary
Decimal

## Slide 30: Example (Binary to Decimal)
1 0 1 0 1 1
1 x 20
1 x 21
0 x 22
1 x 23
0 x 24
1 x 25
+
+
+
+
+
1
2
0
1010112 =
0
32
+
+
+
+
+
4310
4310
8

## Slide 31: Example (Binary to Decimal)
1 1 . 1 1
1 x 20
1 x 21
+
1
2
11.112 =
+
3.7510
3.7510
1 x 2-2
1 x 2-1
+
0.25
0.5
+
+
+

## Slide 32: Exercise
(11011)2 = ( )10
(101101)2 = ( )10
(11101111)2 = ( )10
(110.011)2 = ( )10
(1001.0010)2 = ( )10

## Slide 33: Decimal to Octal
Technique
  Divide by eight
  Keep track of the remainder
Decimal
Octal

## Slide 34: Example (Decimal to Octal)
12510 = ?8
8
125
5
8
15
7
8
1
1
0
12510 =
1758

## Slide 35: Example (Decimal to Octal)
0.687510 = ?8
0.6875 x 8 =
5.5000
5
0.5000
+
0.5000 x 8 =
4.0000
4
0.0000
+
0.687510 =
0.548
integer
fraction

## Slide 36: Exercise
(32)10 = ( )8
(555)10 = ( )8
(12999)10 = ( )8
(157.63)10 = ( )8
(64.125)10 = ( )8

## Slide 37: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Octal
Decimal

## Slide 38: Example (Octal to Decimal)
7 2 4
4 x 80
2 x 81
7 x 82
+
+
7248 =
46810
46810
4
16
448
+
+

## Slide 39: Example (Octal to Decimal)
4 3 . 2 5
3 x 80
4 x 81
+
3
32
43.258 =
+
35.328110
35.328110
5 x 8-2
2 x 8-1
+
0.0781
0.25
+
+
+

## Slide 40: Exercise
(32)8 = ( )10
(555)8 = ( )10
(12333)8 = ( )10
(157.63)8 = ( )10
(64.125)8 = ( )10

## Slide 41: Decimal to Hexa-Decimal
Technique
  Divide by 16
  Keep track of the remainder
Decimal
Hexa-Decimal

## Slide 42: Example (Decimal to HexaDecimal)
123410 = ?16
16
1234
2
123410 =
4D216
16
77
13=D
16
4
4
0

## Slide 43: Exercise
(32)10 = ( )16
(555)10 = ( )16
(12999)10 = ( )16
(157.63)10 = ( )16
(64.125)10 = ( )16

## Slide 44: Hexa-Decimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Hexa-Decimal
Decimal

## Slide 45: Example (HexaDecimal to Decimal)
A B C
C x 160
B x 161
A x 162
+
+
ABC16 =
274810
274810
12 x 160
11 x 161
10 x 162
+
+
12
176
2560
+
+

## Slide 46: Exercise
(FA8)16 = ( )10
(9AC3)16 = ( )10
(1A74D)16 = ( )10
(1AC.9A)16 = ( )10
(ABC.5AC)16 = ( )10

## Slide 47: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation
Octal
Binary

## Slide 48: Octal - Binary Table
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 49: Example (Octal to Binary)
7058 = ?2
7 0 5
101
000
111
7058 =
1110001012

## Slide 50: Exercise
(463)8 = ( )2
(2056)8 = ( )2
(2057.64)8 = ( )2
(6543.04)8 = ( )2
(7476.47)8 = ( )2

## Slide 51: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits
Binary
Octal

## Slide 52: Example (Binary to Octal)
10110101112 = ?8
1
011
001
10110101112 =
13278
111
010
3
2
7

## Slide 53: Exercise
(11011)2 = ( )8
(101101)2 = ( )8
(11101111)2 = ( )8
(110.011)2 = ( )8
(1001.0010)2 = ( )8

## Slide 54: Hexa-Decimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation
Hexa-Decimal
Binary

## Slide 55: Hexa-Decimal to Binary
Hexa-Decimal | Binary | Hexa-Decimal | Binary
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 | A | 1010
3 | 0011 | B | 1011
4 | 0100 | C | 1100
5 | 0101 | D | 1101
6 | 0110 | E | 1110
7 | 0111 | F | 1111

## Slide 56: Example (Hexa-Decimal to Binary)
10AF16 = ?2
1 0 A F
1111
1010
0000
10AF16 =
10000101011112
0001

## Slide 57: Exercise
(FA8)16 = ( )2
(9AC3)16 = ( )2
(1A74D)16 = ( )2
(1AC.9A)16 = ( )2
(ABC.5AC)16 = ( )2

## Slide 58: Binary to Hexa-Decimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits
Binary
Hexa-Decimal

## Slide 59: Example (Binary to Hexa-Decimal)
10110101112 = ?16
0010
10110101112 =
2D716
0111
1101
2
D
7

## Slide 60: Exercise
(11011)2 = ( )16
(101101)2 = ( )16
(11101111)2 = ( )16
(110.011)2 = ( )16
(1001.0010)2 = ( )16

## Slide 61: Octal to Hexa-Decimal
Technique
  Convert Octal to Binary
  Regroup bits in fours from right
  Convert Binary to Hexa-Decimal
Octal
Hexa-Decimal

## Slide 62: Example (Octal to Hexa-Decimal)
10768 = ?16
1 0 7 6
110
111
000
10768 =
23E16
001
1110
0011
0010
E
3
2

## Slide 63: Exercise
(463)8 = ( )16
(2056)8 = ( )16
(2057.64)8 = ( )16
(6543.04)8 = ( )16
(7476.47)8 = ( )16

## Slide 64: Hexa-Decimal to Octal
Technique
  Convert Hexa-Decimal to Binary
  Regroup bits in three from right
  Convert Binary to Octal
Hexa-Decimal
Octal

## Slide 65: Example (Hexa-Decimal to Octal)
1F0C16 = ?8
1 F 0 C
1100
0000
1111
1F0C16 =
174148
0001
100
001
100
4
1
4
111
7
001
1
000
0

## Slide 66: Exercise
(FA8)16 = ( )8
(9AC3)16 = ( )8
(1A74D)16 = ( )8
(1AC.9A)16 = ( )8
(ABC.5AC)16 = ( )8

## Slide 67: Signed Binary Numbers
Two ways of representing signed numbers:
1) Sign-magnitude form, 2) Complement form.
Most of computers use complement form for negative number notation.
1’s complement and 2’s complement are two different methods in this type.

## Slide 68: 1’s Complement
1
1
1
1
1
1
0
1
0
0
1
0
-
(1’s complement of 1101)
1
1
1
.
1
0
1
.
0
1
0
.
-
(1’s complement of 101.01)
1
1
0
1
1
0
1’s complement of a binary number is obtained by subtracting each digit of that binary number from 1.
Example

## Slide 69: 2’s Complement
2’s complement of a binary number is obtained by adding 1 to its 1’s complement.
1
1
1
1
1
1
0
0
0
0
1
1
-
(2’s complement of 1100)
0
1
0
.
-
(2’s complement of 101.01)
1
1
1
.
1
1
1
0
1
.
0
1
1
0
1
0
1
0
0
1
+
+
0
1
0
1
1
.
Example

## Slide 70: Representation of negative number in 2’s complement form
Express -65.5 in 12 bit 2’s complement form.
2
65
1
2
32
0
2
16
0
2
8
0
2
4
0
2
2
0
2
1
1
0
0.5 x 2 =
1.0
65.510 =
01000001.10002
So, result in 12-bit binary is as follows:
For negative number, we have to convert this into 2’s complement form
-65.510 =
10111110.10002

## Slide 71: Exercise
Express -45 in 8-bit 2’s complement form.
Express -73.75 in 12 bit 2’s complement form.

## Slide 72: Accuracy in Binary Number Conversion
Convert (0.252)10 to binary with an error less than 1%.
Solution
Absolute value of allowable error is found by calculating 1% of the number
Maximum error due to truncation is set to be less than allowable error by solving from . This equation is written as
Inverting both sides of the inequality

## Slide 73: Accuracy in Binary Number Conversion
Taking log of both sides and solving for
This indicates that the use of 9 bits in the binary number will guarantee an error less than 1%.
So the conversion is carried out to 9 places which results in

## Slide 74: 9’s Complement
9’s complement of a decimal number is obtained by subtracting each digit of that decimal number from 9.
9
9
9
9
3
4
6
5
6
5
3
4
-
(9’s complement of 3465)
9
9
9
.
7
8
2
.
2
1
7
.
-
(9’s complement of 782.54)
9
9
5
4
4
5
Example

## Slide 75: 10’s Complement
10’s complement of a decimal number is obtained by adding 1 to its 9’s complement.
9
9
9
9
3
4
6
5
6
5
3
4
-
(10’s complement of 3465)
2
1
7
.
-
(10’s complement of 782.54)
9
9
9
.
9
9
7
8
2
.
5
4
4
5
1
6
5
3
5
1
+
+
2
1
7
4
6
.
Example

## Slide 76: Subtraction using 9’s complement
Obtain 9’s complement of subtrahend
Add the result to minuend and call it intermediate result
If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
If there is no carry then answer is negative and take 9’s complement of intermediate result and place negative sign to the result.

## Slide 77: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
1) 745.81 – 436.62
7
4
5
.
8
1
5
6
3
.
+
3
7
3
0
9
.
1
1
8
+
1
3
0
9
.
1
9
3
0
9
.
1
9
9’s complement

## Slide 78: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
2) 436.62 - 745.81
2
5
4
.
+
1
8
6
9
0
.
8
0
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
9’s complement
9’s complement
As carry is not generated, so take 9’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 79: Subtraction using 10’s complement
Obtain 10’s complement of subtrahend
Add the result to minuend
If carry is generated then ignore it and result itself is answer
If there is no carry then answer is negative and take 10’s complement of result and place negative sign to the result.

## Slide 80: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
1) 745.81 – 436.62
5
6
3
.
+
7
4
5
.
8
1
3
8
3
0
9
.
1
1
9
3
0
9
.
1
9
Ignore the carry
10’s complement

## Slide 81: Example
7
4
5
.
4
3
6
.
-
8
1
6
2
2) 436.62 - 745.81
2
5
4
.
+
1
9
6
9
0
.
8
1
3
0
9
.
1
9
3
0
9
.
1
9
-
4
3
6
.
6
2
-
10’s complement
10’s complement
As carry is not generated, so take 10’s complement of the intermediate result and add ‘ – ‘ sign to the result

## Slide 82: Binary Addition
Rules for binary addition
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10 i.e. 0 with a carry of 1
1
1
0
1
0
1
1
1
0
1
0
1
1
1
1
1
1
+
.
1
0
1
.
0
1
1
.
0
0
0
1
1

## Slide 83: Binary Subtraction
Rules for binary subtraction
0 – 0 = 0
1 – 1 = 0
1 – 0 = 1
0 – 1 = 1, with a borrow 1
1
0
1
0
0
1
1
1
0
0
1
0
-
.
0
1
0
.
1
1
1
.
0
1
1
1
0
1
1
1
0
1
1
0

## Slide 84: Binary Multiplication
1 0 1 1 1
1 0 0 1 1
x
1
1
1
0
1
1
1
1
0
1
0
0
0
0
0
0
0
0
0
0
1
1
1
0
1
1
0
1
0
1
1
0
1
1

## Slide 85: Binary Division
1 0 1 1 0 1
110
0
0 0 0
1 0 1
1
1 1 0
1 0 1
0
1 1 0
1 0 0
1
1 1 0
1 1
1
1
1
.
1
0
1 1 0
0 0 0

## Slide 86: Subtraction using 1’s Complement
Obtain 1’s complement of subtrahend
Add the result to minuend and call it intermediate result
If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
If there is no carry then answer is negative and take 1’s complement of intermediate result and place negative sign to the result.

## Slide 87: Example
6
8
.
2
7
.
-
7
5
5
0
1) 68.75 – 27.50
+
4
1
.
2
5
1’s complement
0
0
0
.
1
1
1
0
0
0
1
0
0
+
1
0
0
.
1
0
0
1
1
0
1
1
1
+
1
0
0
1
.
1
0
0
0
1
0
0
1
1
1
0
1
0
.
0
1
0
0
1
0
1
0
0

## Slide 88: Example
2) 43.25 - 89.75
As carry is not generated, so take 1’s complement of the intermediate result and add ‘ – ‘ sign to the result
4
3
.
8
9
.
-
2
5
7
5
-
4
6
.
5
0
1’s complement
1
0
1
.
0
1
0
1
1
0
0
0
0
+
1
0
0
.
1
1
0
1
0
0
0
1
1
0
0
1
.
0
0
1
1
0
1
1
1
1
1
1
0
.
1
1
0
0
1
0
0
0
0
1’s complement

## Slide 89: Subtraction using 2’s Complement
Obtain 2’s complement of subtrahend
Add the result to minuend
If carry is generated then ignore it and result itself is answer
If there is no carry then answer is negative and take 2’s complement of result and place negative sign to the result.

## Slide 90: Example
6
8
.
2
7
.
-
7
5
5
0
1) 68.75 – 27.50
+
4
1
.
2
5
2’s complement
0
0
0
.
1
1
1
0
0
0
1
0
0
+
1
0
0
.
1
0
0
1
1
1
0
0
0
0
0
1
.
1
0
1
0
1
0
0
1
0
0
0
0
1
.
1
0
1
0
1
0
0
0
0
Ignore Carry bit

## Slide 91: Example
2) 43.25 - 89.75
As carry is not generated, so take 2’s complement of the intermediate result and add ‘ – ‘ sign to the result
4
3
.
8
9
.
-
2
5
7
5
-
4
6
.
5
0
2’s complement
1
0
1
.
0
1
0
1
1
0
0
0
0
+
1
0
0
.
1
1
0
1
0
0
1
0
0
0
0
1
.
0
1
0
1
0
1
1
0
0
1
1
0
.
1
1
0
0
1
0
0
0
0
2’s complement

## Slide 92: Binary Codes
Unit – 1: Binary Systems & Logic Circuits Darshan Institute of Engineering & Technology

## Slide 93: 8421 BCD Code (Natural BCD Code)
Each decimal digit, 0 through 9, is coded by 4-bit binary number
8, 4, 2 and 1 weights are attached to each bit
BCD code is weighted code
1010, 1011, 1100, 1101, 1110 and 1111 are illegal codes
Less efficient than pure binary
Arithmetic operations are more complex than in pure binary
Example
1 4
0100
0001
Decimal
BCD
Binary
1110

## Slide 94: Binary Codes
Decimal | Binary | BCD
0 | 0 | 0000
1 | 1 | 0001
2 | 10 | 0010
3 | 11 | 0011
4 | 100 | 0100
5 | 101 | 0101
6 | 110 | 0110
7 | 111 | 0111
Decimal | Binary | BCD
8 | 1000 | 1000
9 | 1001 | 1001
10 | 1010 | 0001 0000
11 | 1011 | 0001 0001
12 | 1100 | 0001 0010
13 | 1101 | 0001 0011
14 | 1110 | 0001 0100
15 | 1111 | 0001 0101

## Slide 95: BCD Addition
0
0
1
0
0
0
0
1
0
0
1
1
+
0
1
0
1
0
0
1
1
1
0
0
0
2
5
1
3
+
3
8
No carry, no illegal code. So, this is the correct sum.

## Slide 96: BCD Addition
0110
0111
1001
+
.0110
679.6
536.8
+
1216.4
All are illegal codes
0101
0011
0110
.1000
1011
1010
1111
.1110
+0110
+0110
+0110
+.0110
10001
10000
10101
1.0100
1
+
1
+
1
+
1
+
0010
0001
0110
.0100
0001
Add 0110 to each
Propagate carry
Corrected Sum

## Slide 97: BCD Subtraction
0
0
1
1
0
0
0
1
0
0
1
0
-
1
0
0
0
0
1
0
1
0
0
1
1
3
8
1
5
-
2
3
No borrow. So, this is the correct difference.

## Slide 98: BCD Subtraction
0010
0000
0110
-
.0111
206.7
147.8
-
58.9
Borrows are present
0001
0100
0111
.1000
0000
1011
1110
.1111
-0110
-0110
-.0110
0101
1000
.1001
Subtract 0110
Corrected difference

## Slide 99: Excess Three (XS-3) Code
Excess Three Code = 8421 BCD + 0011(3)
XS-3 code is non-weighted BCD code
Also known as self complementing code
0000, 0001, 0010, 1101, 1110 and 1111 are illegal codes
Example
1 4
0100
0001
Decimal
BCD
XS-3
0100
0111

## Slide 100: XS-3 Addition
0
1
1
0
0
1
0
1
1
0
1
1
+
1
0
1
0
1
0
1
1
0
1
0
1
3
7
2
8
+
6
5
Propagate carry to next group
1
1
+
0
1
0
1
1
1
0
0
0
0
1
1
+
0
0
1
1
-
1
0
0
0
1
0
0
1
Add 0011 to group which generated carry
Subtract 0011 to group which do not generated carry

## Slide 101: XS-3 Addition
0101
0111
1010
+
.1001
247.6
359.4
+
607.0
Carry generated
0110
1000
1100
.0111
1011
1111
10110
1.0000
- 0011
+0011
+0011
+.0011
1011
10000
0111
.0000
1
+
1
+
1
+
Propagate carry
.0000
0111
0000
1100
Add 0011 to group which generated carry
Subtract 0011 to group which do not generated carry
Corrected Sum in XS-3
.0011
1010
0011
1001

## Slide 102: XS-3 Subtraction
0101
1001
1010
-
267
175
-
092
0100
1010
1000
0000
1111
0010
-0011
+0011
0011
1100
0101
Subtract 0011 to group which generated borrow
Add 0011 to group which do not generated borrow
+0011

## Slide 103: XS-3 Subtraction
1000
1010
.1001
-
57.6
27.8
-
29.8
0101
1010
.1011
0010
1111
.1110
-0011
+0011
0101
1100
.1011
Subtract 0011 to group which generated borrow
Add 0011 to group which do not generated borrow
-.0011

## Slide 104: Gray Code
Only one bit changes between each pair of successive code words (Unit distance code).
Gray code is a reflected code.
Gray codes are designed recursively using following rules:
  1-bit Gray code has two code words, 0 and 1.
  The first 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, written in order with a leading 0 appended.
  The last 2n code words of an (n+1)-bit Gray code equal the code words of n-bit gray code, but written in reverse order with a leading 1 appended.

## Slide 105
Gray Code |  |  |  | Decimal | 4-bit Binary
1-bit | 2-bit | 3-bit | 4-bit |  | 
0 | 0 0 | 0 0 0 | 0 0 0 0 | 0 | 0000
1 | 0 1 | 0 0 1 | 0 0 0 1 | 1 | 0001
 | 1 1 | 0 1 1 | 0 0 1 1 | 2 | 0010
 | 1 0 | 0 1 0 | 0 0 1 0 | 3 | 0011
 |  | 1 1 0 | 0 1 1 0 | 4 | 0100
 |  | 1 1 1 | 0 1 1 1 | 5 | 0101
 |  | 1 0 1 | 0 1 0 1 | 6 | 0110
 |  | 1 0 0 | 0 1 0 0 | 7 | 0111
 |  |  | 1 1 0 0 | 8 | 1000
 |  |  | 1 1 0 1 | 9 | 1001
 |  |  | 1 1 1 1 | 10 | 1010
 |  |  | 1 1 1 0 | 11 | 1011
 |  |  | 1 0 1 0 | 12 | 1100
 |  |  | 1 0 1 1 | 13 | 1101
 |  |  | 1 0 0 1 | 14 | 1110
 |  |  | 1 0 0 0 | 15 | 1111

## Slide 106: Binary to Gray Conversion
Conversion of n-bit Binary number (B) to Gray Code (G) is as follows:
Example: Convert (1001)2 to Gray Code.
1
Binary
Gray
0
0
1
1
1
0
1

## Slide 107: Gray to Binary Conversion
Conversion of n-bit Gray Code (G) to Binary Number (B) is as follows:
Example: Convert Gray code 1101 to Binary.
1
Gray
Binary
1
0
1
1
0
0
1

## Slide 108: Error-Detecting Codes
Noise can alter or distort the data in transmission.
The 1s may get changed to 0s and 0s to 1s.
Because digital systems must be accurate to the digit, errors can pose a serious problem.
Single bit error should be detect & correct by different schemes.
Parity, Check Sums and Block Parity are the examples of error detecting code.

## Slide 109: Parity
Parity bit is the simplest technique.
There are two types of parity – Odd parity and Even parity.
For odd parity, the parity is set to a 0 or a 1 at the transmitter such that the total number of 1 bits in the word including the parity bit is an odd number.
For even parity, the parity is set to a 0 or a 1 at the transmitter such that the total number of 1 bits in the word including the parity bit is an even number.
For example, 0110 binary number has “1” as Odd parity and “0” as even parity.

## Slide 110: Parity
Detect a single-bit error but can not detect two or more errors within the same word.
In any practical system, there is always a finite probability of the occurrence of single error.
E.g. In an even-parity scheme, code 10111001 is erroneous because number of 1s is odd(5), while code 11110110 is error free because number of 1s is even(6).

## Slide 111: Check Sums
Simple parity can not detect two errors within the same word.
Added to the sum of the previously transmitted words
At the transmission, the check sum up to that time is sent to the receiver.
The receiver can check its sum with the transmitted sum.
If the two sums are the same, then no errors were detected at the receiver end.
If there is an error, the receiving location can ask for retransmission of the entire data.
This type of transmission is used in teleprocessing system.

## Slide 112: Block Parity
01011011
10010101
01101110
11010011
10001101
01110111
0
1
0
0
1
1
0
01110110
Parity Column
Parity Row
01011011
10010101
01100110
11010011
10001101
01110111
0
1
0
0
1
1
0
01110110
01011011
10010101
01101110
10000011
10001101
01110111
0
1
0
0
1
1
0
01110110

## Slide 113: Error Correcting Code
7-bit Hamming Code is widely used error correcting code, containing 4 bits of data and 3 bits of even parity.
Pattern: P1 P2 D3 P4 D5 D6 D7
Group-1: P1D3D5D7, Group-2: P2D3D6D7, Group-3: P4D5D6D7
Example: Data = 1101
P1 P2 D3 P4 D5 D6 D7 = P1 P2 1 P4 1 0 1
P1 D3 D5 D7 = 1 1 1 1
P2 D3 D6 D7 = 0 1 0 1
P4 D5 D6 D7 = 0 1 0 1
7-bit Hamming Code is 1 0 1 0 1 0 1

## Slide 114: Error Correcting Code
How to detect error?
Example: Received data = 1001001
P1 P2 D3 P4 D5 D6 D7 = 1 0 0 1 0 0 1
P1 D3 D5 D7 = 1 0 0 1 (No Error)
P2 D3 D6 D7 = 0 0 0 1 (Error)
P4 D5 D6 D7 = 1 0 0 1 (No Error)
The error word is 0 1 0 = 210.
Complement the 2nd bit (from left).
Correct code is 1 1 0 1 0 0 1

## Slide 115: Digital IC Specification
Threshold voltage
Propagation Delay
Power dissipation
Fan-in
Fan-out
Voltage & Current parameters
Noise Margin
Operating Temperatures
Speed power products

## Slide 116: TTL v/s CMOS v/s ECL
Characteristic | TTL | CMOS | ECL
Power Input | Moderate | Low | Moderate-High
Frequency limit | High | Moderate | Very high
Circuit density | Moderate-high | High-very high | Moderate
Circuit types per family | High | High | Moderate
Logic Family | Propagation delay time (ns) | Power dissipation per gate (mW) | Noise Margin (V) | Fan-in | Fan-out | Cost
TTL | 9 | 10 | 0.4 | 8 | 10 | Low
CMOS | <50 | 0.01 | 5 | 10 | 50 | Low
ECL | 1 | 50 | 0.25 | 5 | 10 | High

## Slide 117: Transistor Transistor Logic (TTL)
Dependence on transistors alone to perform basic logic operations.
Most popular logic family.
Most widely useful bipolar digital IC family.
The TTL uses transistors operating in saturated mode.
It is the fastest of the saturated logic families.
Good speed, low manufacturing cost, wide range of circuits, and the availability in SSI and MSI are its merits.

## Slide 118: Schottky TTL
When a transistor is saturated, excess charge carries will be stored in the base region and they must be removed before the transistor can be turned off.
So, owing to storage time delay, the speed is reduced.
The Schottky TTL series reduces this storage time delay by not allowing the transistor to go into full saturation.
This is accomplished by using a Schottky barrier diode(SBD) between the base and the collector of each transistor.
More than three times the switching speed of standard TTL, at the expense of approximately doubling the power consumption.

## Slide 119: Tri-state TTL
It utilizes the advantage of the high speed of operation of the totem-pole configuration and wire ANDing of the open-collector configuration.
It is called the tri-state TTL, because it allows three possible output states: HIGH, LOW, and HIGH Impedance (Hi-Z).
In the Hi-Z state, both the transistors in the totem-pole arrangement are turned off, so that the output terminal is a HIGH impedance to ground or Vcc.
In fact, the output is an open or floating terminal, that is, neither a LOW nor a HIGH.