## Slide 1
Prof. Krunal D. Vyas
9601901005
krunal.vyas@darshan.ac.in
3130704
Digital Fundamentals
Module 4:
A/D and D/A Converters

## Slide 2: Topics to be covered
Digital to analog converters
Specifications for D/A converters
Sample and hold circuit
Analog to digital converters
Specifications for A/D converters
Example of D/A converter ICs and A/D converter ICs

## Slide 3: Digital to analog converter
Converts straight binary or BCD code into a voltage or current which is proportional to the digital value.
Fig shows the symbol for a typical 4-bit D/A converter.
D
C
B
A
MSB
LSB
Digital
Inputs
Vout
Analog
output
D/A
Converter
(DAC)

## Slide 4: Weighted-resistor type DAC
R
2R
4R
8R
_
+
Rf
I
I
Vout = - (D3 + D2 + D1 + D0)
(MSB)D3
D2
D1
(LSB)D0
The main disadvantage is that a different-valued precision resistor must be used for each bit position of the digital input.

## Slide 5: Weighted-resistor type DAC
Example:- For the weighted-resistor DAC, determine (a) the weight of each input bit if the inputs are 0 V and 5 V, (b) the full-scale output, if Rf = R = 1 kΩ.
Solution:-
(a) If MSB passes with a gain of 1. so, its weight = 5 V; the next bit passes with a gain of 1/2. so, its weight = 2.5 V; the following bit passes with a gain of 1/4. so, its weight = 1.25 V; the LSB passes with a gain of 1/8. so, its weight = 0.625 V.
(b) Therefore, the full-scale output when Rf = R = 1 kΩ
= - 9.375 V

## Slide 6: R-2R ladder type DAC
_
+
R
R
R
2R
2R
2R
2R
2R
(MSB)D3
D2
D1
(LSB)D0
Vout = Analog output
+

## Slide 7: R-2R ladder type DAC
Case 1: Input is 1000
R
R
R
2R
2R
2R
2R
2R
D3
D2
D1
D0
Vout
+E
2R
Vout
+E
2R
+
+
2R
2R
E
Vout = E/2
A

## Slide 8: R-2R ladder type DAC
Case 2: Input is 0100
R
2R
2R
2R
Vout
+E
+
2R
2R
E
R
A
B
A
B
i1
2R
2R
E/2
Vout = E/4

## Slide 9: R-2R ladder type DAC
Case 3: Input is 0010
R
R
2R
2R
2R
2R
Vout
+
A
B
C
+E
2R
E
A
B
i2
2R
R
R
2R
i1
C
2R
2R
E/4
Vout = E/8

## Slide 10: R-2R ladder type DAC
Case 4: Input is 0001
2R
E
A
B
i3
2R
R
R
R
i2
C
2R
2R
i1
2R
2R
E/8
Vout = E/16

## Slide 11: Specifications for DAC
1) Resolution:-
Smallest change that can occur in an analog output as a result of a change in the digital input.
Equals to the weight of the LSB and also referred to as the step size.
Step size is the amount by which Vout will change as the digital input value is changed from one value to the next.
% resolution = step size / full scale x 100%
Full-scale = No. of steps x step size,
% resolution = 1 / No. of steps x 100%

## Slide 12: Specifications for DAC
2) Accuracy:-
Specified in terms of full-scale error and linearity error
Full-scale error is the maximum deviation of DAC’s output from its expected value.
Linearity error is the maximum deviation of the analog output from the ideal output.

## Slide 13: Specifications for DAC
3) Settling time:-
The time required for the analog output to settle to within ± ½ LSB of the final value after a change in the digital input.
It is because of the presence of switches, active devices, stray capacitance, and inductance.
4) Offset voltage:-
Ideally, the output of a DAC should be zero when the binary input is zero.
However, in practice, there is a very small output voltage under this situation called the offset voltage.

## Slide 14: Specifications for DAC
5) Monotonicity:-
This means that the staircase output will have no downward steps as the binary input is incremented from 0 to full-scale value.
6) Temperature sensitivity:-
The analog output voltage for any fixed digital input varies with temperature.

## Slide 15: Specifications for DAC
Example:- An 8-bit DAC produces Vout = 0.05 V for a digital input of 00000001. Find the full-scale output. What is the resolution? What is Vout for an input of 00101010?
Solution:-
Full-scale output = Step size x No. of steps
= 0.05 x (28 – 1) = 0.05 x 255 = 12.75 V
% resolution = 1 / 255 x 100 %
= 0.392 %
Vout for an input of 00101010 = 42 x 0.05
= 2.10 V

## Slide 16: Sample and hold circuit
Vi
Vo
S
Basic Sample and hold circuit
Vi
Vo
S
_
+
_
+
Analog
input
DC
output
Clock
Digitally
Controlled
switch
Practical Sample and hold circuit

## Slide 17: Quantization and encoding
0 V
1/8 V
2/8 V
3/8 V
4/8 V
5/8 V
6/8 V
7/8 V
1 V
000
001
010
011
100
101
110
111

## Slide 18: Parallel comparator A/D converter
_
+
_
+
_
+
_
+
_
+
_
+
_
+
EREF
Analog input
Priority
encoder
D2
D1
D0
Digital
output
R
R
R
R
R
R
R
R
7/8 EREF
6/8 EREF
5/8 EREF
4/8 EREF
3/8 EREF
2/8 EREF
1/8 EREF
8 V
3.7 V
L
L
L
L
H
H
H
0
1
1

## Slide 19: Successive approximation type ADC
_
+
VA
Analog
input
Comparator
Control
logic
Output
register
DAC
VAX
CLK
START
EOC
MSB
LSB
Binary output
10.3 V
1000
8 V
8 V
HIGH
1100
12 V
12 V
LOW
1010
10 V
10 V
1011
11 V
11 V

## Slide 20: Dual-slope type ADC
_
+
_
+
Binary
counter
Control
circuitry
Binary output
Counter
control
R
C
CLK
CLK
Analog
input
EREF
Switch control
Voltage
comparator
Integrator
t
V

## Slide 21: Counter-type ADC
_
+
CLK
Q7
Q6
Q5
Q4
Q3
Q2
Q1
Q0
D7
D6
D5
D4
D3
D2
D1
D0
Divide by-256 counter
D/A converter
8-bit
latch
Control
Comparator
Analog
input
Staircase
Reference voltage
Clear
8-bit
Digital
output

## Slide 22: Counter-type ADC
Time (s)
Voltage
1
2
3
4
5
6
1000
0110
1000
Analog input
Counter reset
Staircase reference voltage

## Slide 23: A/D converter using voltage to frequency conversion
_
+
_
+
Monostable
Multi-vibrator
Binary
Counter
B0
B1
BN-1
Va
R
C
S
-VR
VEN
Vc
Binary
Output
Vo

## Slide 24: A/D converter using voltage to time conversion
_
+
_
+
Binary
Counter
B0
B1
BN-1
Va
R
C
S
-VR
Clock
Vc
Binary
Output
Vo
VEN
Clock

## Slide 25: Specifications for ADC
Range of input voltage
Input impedance
Accuracy
Conversion time
Format of digital output