## Slide 1
Prof. Krunal D. Vyas
96019 01005
krunal.vyas@darshan.ac.in
3140707
Computer Organization & Architecture
Unit – 3 Programming the Basic Computer

## Slide 2: Topics to be covered
Introduction
Machine Language
Assembly Language
Assembler
Program loops
Programming Arithmetic and logic operations
Subroutines
I-O Programming

## Slide 3: Machine Language
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 4: Machine Language
Program
A program is a list of instructions or statements for directing the computer to perform a required data-processing task.

## Slide 5: Categories of programs
Binary code
This is a sequence of instructions and operands in binary that list the exact representation of instructions as they appear in computer memory.
Location | Instruction Code |  |  | 
0 | 0010 | 0000 | 0000 | 0100
1 | 0001 | 0000 | 0000 | 0101
10 | 0011 | 0000 | 0000 | 0110
11 | 0111 | 0000 | 0000 | 0001
100 | 0000 | 0000 | 0101 | 0011
101 | 1111 | 1111 | 1110 | 1001
110 | 0000 | 0000 | 0000 | 0000

## Slide 6: Categories of programs
Octal or hexadecimal code
This is an equivalent translation of the binary code to octal or hexadecimal representation.
Location | Instruction
000 | 2004
001 | 1005
002 | 3006
003 | 7001
004 | 0053
005 | FFE9
006 | 0000

## Slide 7: Categories of programs
Symbolic code
  The user employs symbols (letters, numerals, or special characters) for the operation part, the address part, and other parts of the instruction code.
  Each symbolic instruction can be translated into one binary coded instruction by a special program called an assembler and language is referred to as an assembly language program.
Location | Instruction | Comment
000 | LDA 004 | Load first operand into AC
001 | ADD 005 | Add second operand to AC
002 | STA 006 | Store sum in location 006
003 | HLT | Halt computer
004 | 0053 | First operand
005 | FFE9 | Second operand (negative)
006 | 0000 | Store sum here

## Slide 8: Categories of programs
High-level programming languages
  These are special languages developed to reflect the procedures used in the solution of a problem rather than be concerned with the computer hardware behavior. E.g. Fortran, C++, Java, etc.
  The program is written in a sequence of statements in a form that people prefer to think in when solving a problem.
  However, each statement must be translated into a sequence of binary instructions before the program can be executed in a computer.
INTEGER A, B, C
DATA A, 83 B,-23
C = A + B
END

## Slide 9: Assembly Language
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 10: Pseudo Instruction
A pseudo instruction is not a machine instruction but rather an instruction to the assembler giving information about some phase of the translation.
Symbol | Information for the Assembler
ORG N | Hexadecimal number N is the memory location for the instruction or operand listed in the following line.
END | Denotes the end of symbolic program.
DEC N | Signed decimal number N to be converted to binary.
HEX N | Hexadecimal number N to be converted to binary

## Slide 11: Assembler
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 12: Assembler
An assembler is a program that accepts a symbolic language program and produces its binary machine language equivalent.
The input symbolic program is called the source program and the resulting binary program is called the object program.
The assembler is a program that operates on character strings and produces an equivalent binary interpretation.

## Slide 13: A.L.P. to subtract 2 numbers
Location |  | Instruction
 |  | ORG 100
100 |  | LDA SUB
101 |  | CMA
102 |  | INC
103 |  | ADD MIN
104 |  | STA DIF
105 |  | HLT
106 | MIN, | DEC 83
107 | SUB, | DEC -23
108 | DIF, | HEX 0
 |  | END
Symbol | Location
MIN | 106
SUB | 107
DIF | 108

## Slide 14: First Pass of an assembler
LC ← 0
Scan next line of code
Label
Store address in symbol table together with value of LC
Increment LC
Set LC
ORG
END
Go to second pass
First pass
no
no
no
yes
yes
yes

## Slide 15
LC ← 0
Scan next line of code
Pseudo-instruction
Store binary equivalent of instruction in location given by LC
Increment LC
Set LC
ORG
END
Second pass
Yes
No
No
No
Yes
Yes
Done
Convert operand to binary and store in location given by LC
MRI
No
Valid non-MRI instruction
Get operation code and set bits 2-4
Search address-symbol table for binary equivalent of symbolic address and set bits 5-16
I
Set first bit to 1
Set first bit to 0
Yes
No
Assemble all parts of binary instruction and store in location given by LC
Yes
Error in line of code
No
Yes
Second Pass
of an assembler
DEC or HEX

## Slide 16: Program Loops
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 17: Program Loops
A program loop is a sequence of instructions that are executed many times, each time with a different set of data.
A system program that translates a program written in a high-level programming language to a machine language program is called a compiler.

## Slide 18: A.L.P. to Add 100 Numbers
1
ORG 100
/Origin of program is HEX 100
2
LDA ADS
/Load first address of operands
3
STA PTR
/Store in pointer
4
LDA NBR
/Load minus 100
5
STA CTR
/Store in counter
6
LOP,
CLA
/Clear accumulator
7
ADD PTR I
/Add an operand to AC
8
ISZ PTR
/Increment pointer
9
ISZ CTR
/Increment counter
10
BUN LOP
/Repeat loop again
11
STA SUM
/Store sum
12
HLT
/Halt

## Slide 19: A.L.P. to Add 100 Numbers
ADS,
13
HEX 150
/First address of operands
PTR,
14
HEX 0
/This location reserved for pointer
NBR,
15
DEC -100
/Constant to initialized counter
CTR,
16
HEX 0
/This location reserved for a counter
SUM,
17
HEX 0
/Sum is store here
18
ORG 150
/Origin of operands is HEX 150
19
DEC 75
/First operand
118
DEC 23
/Last operand
119
END
/End of symbolic program
.
.
.

## Slide 20: A.L.P. to clear the contents of hex locations 500 to 5FF with 0
1
ORG 100
/Origin of program is HEX 100
2
LDA ADS
/Load first address of operands
3
STA PTR
/Store in pointer
4
LDA NBR
/Load minus 255
5
STA CTR
/Store in counter
6
LOP,
CLA
/Clear accumulator
7
STA PTR I
/Store zero to location pointed by PTR
8
ISZ PTR
/Increment pointer
9
ISZ CTR
/Increment counter
10
BUN LOP
/Repeat loop again
11
HLT
/Halt
ADS,
12
HEX 500
/First address of operands
PTR,
13
HEX 0
/This location reserved for pointer
NBR,
14
DEC -255
/Constant to initialized counter
CTR,
15
HEX 0
/This location reserved for a counter
16
END
/End of symbolic program

## Slide 21: Programming Arithmetic and Logic Operation
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 22: A.L.P. to Add Two Double-Precision Numbers
1
ORG 100
/Origin of program is HEX 100
2
LDA AL
/Load A low
3
ADD BL
/Add B low, carry in E
4
STA CL
/Store in C low
5
CLA
/Clear AC
6
CIL
/Circulate to bring carry into AC(16)
7
ADD AH
/Add A high and carry
8
ADD BH
/Add B high
9
STA CH
/Store in C high
10
HLT
/Halt

## Slide 23: Subroutines
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 24: Subroutine
A set of common instructions that can be used in a program many times is called a subroutine.
Each time that a subroutine is used in the main part of the program, a branch is executed to the beginning of the subroutine.
After the subroutine has been executed, a branch is made back to the main program.
A subroutine consists of a self contained sequence of instructions that carries a given task.

## Slide 25: A.L.P. to demonstrate Subroutine
ORG 100
100
LDA X
101
BSA SH4
102
STA X
103
LDA Y
104
BSA SH4
105
STA Y
106
HLT
107
HEX 1234
X,
108
HEX 4321
Y,
109
HEX 0
10A
CIL
10B
CIL
10C
CIL
10D
CIL
10E
AND MSK
10F
BUN SH4 I
110
HEX FFF0
MSK,
END
SH4,

## Slide 26: I-O Programming
Unit – 3: Programming Basic Computer Darshan Institute of Engineering & Technology

## Slide 27: A.L.P. to input one character
1
ORG 100
/Origin of program is HEX 100
2
SKI
/Check input flag
3
BUN CIF
/Flag = 0, branch to check again
4
INP
/Flag = 1, input character
5
OUT
/Print character
6
CHR,
STA CHR
/Store character
7
HLT
8
-
/Store character here
9
END
CIF,

## Slide 28: A.L.P. to output one character
1
ORG 100
/Origin of program is HEX 100
2
LDA CHR
/Load character into AC
3
SKO
/Check output flag
4
BUN COF
/Flag = 0, branch to check again
5
OUT
/Flag = 1, output character
CHR,
6
HLT
7
HEX 0057
/Character is “W”
8
END
COF,

## Slide 29: Questions asked in GTU exam
What is an Assembler? With clear flowcharts for first and second pass, explain its working.
Write an assembly language program to add 10 numbers from memory.
Write a brief note on: Subroutine call and return.
Write an ALP for multiplying 3 integers stored in register stack.
Write an assembly program to multiply two positive numbers.
What is machine language? How it differs from assembly language?
Define pseudo-instruction.
For the following C language code, write assembly language program:
int a, b, c;
a = 83; //plus 83
b = -23; //minus 23
c = a + b;