## Slide 1: Unit-5 Application Building with IoT
Kalpesh.surati@darshan.ac.in
+91 99250 10033
Computer Engineering Department
Prof. Kalpesh H Surati
IOT and Applications
GTU # 3160716

## Slide 2: Applications with IoT
Overview
Using IoT we can build many applications but here, few IoT Applications will be discussed.
We will cover following topics of the IoT applications.
  Overview – General Practice
  Importance – Why we need?
  Requirements – Materials and Facility
  Architecture – Functional Block Diagram
  How it works – General Working of IoT Applications
Before we explore them one by one, let’s understand the common architecture of the IoT applications.

## Slide 3: Applications with IoT
Internet
Within Organization for
Local Analysis, Processing and Controlling
Common Architecture for IoT Application
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Where, Link: Wire, LAN, Wi-Fi, or Bluetooth Connectivity
Controller Node
Link
Fog / Local Computer
Link
Sensor Nodes
All Kind of Sensors,
GPS, etc.
Actuator Nodes
Relays, Alarms, Motors, Actuators, Light Indicators, etc.
Local Monitoring
Link
In House Monitoring or Care Taker Team Members
Remote Monitoring
Data Analytics
Research / Decision Making
Internet
Remote Monitoring or Care Taker or Emergency Help Team Members.
This “Local Analysis, Processing and Controlling” section may not be there in many IoT solutions

## Slide 4: Applications with IoT
Internet
Within Organization for
Local Analysis, Processing and Controlling
Common Architecture for IoT Application
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Where, Link: Wire, LAN, Wi-Fi, or Bluetooth Connectivity
Controller Node
Link
Fog / Local Computer
Link
Actuator Nodes
Relays, Alarms, Motors, Actuators, Light Indicators, etc.
Sensor Nodes
All Kind of Sensors, GPS, etc.
Local Monitoring
Link
In House Monitoring or Care Taker Team Members
Remote Monitoring
Data Analytics
Research / Decision Making
Internet
Remote Monitoring or Care Taker or Emergency Help Team Members.
This Local Analysis, Processing and Controlling section may not be there in many IoT solution

## Slide 5: Applications with IoT
How it works
All the sensor and actuator nodes should be placed at appropriate place.
The sensor and actuator nodes should have proper connectivity with controller nodes or direct to the cloud server.
The sensor nodes sends the sensed data to the controller nodes or directly to the cloud server.
The controller node
  Collects the data from all the sensors,
  Apply some business logic on it as per the requirements and
  Send it to the Fog or local computer, or directly to the cloud server.
Gateway
Actuator Node
Sensor Node
Sensor Node
Sensor Node
Actuator Node

## Slide 6: Applications with IoT
How it works
All the controller nodes should have connected with the Fog or local computer network, or directly to the cloud server via Internet.
Fog or local computer
  Receives all the data from all the controller nodes,
  Execute some business logic and
  Do analysis on the collected data, and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the local team.
The Fog computer should have Internet connectivity for the cloud communication.

## Slide 7: Applications with IoT
How it works
All the in House Monitoring team members can access status of all the sensors from the Fog/Local computer.
The cloud
  Stores all the data received from the Fog/Local computer or directly from the sensors,
  Execute some business logic and
  Do analysis on the stored data.
All those who have rights to access the cloud data can get desire information from it, like
  Remote monitoring team members,
  Data analytics team

## Slide 8: Applications with IoT
How it works
The care taker and data analytics teams may execute corrective action based on the analyzed data.
They may
  Send command to the local computer or to the actuators directly and
  Broadcast alert messages to the concern persons.
All the actuator nodes receives command from the cloud directly or from the controller or local computer.
The “Local Analysis, Processing and Controlling” section may not be there in many IoT solution.

## Slide 9: Healthcare Application with IoT
Overview
The healthcare sector consists of medical and related goods and services.
Healthcare sector provides medical services for maintaining or improving health via
  Prevention
  Diagnosis
  Treatment
  Recovery or cure of disease, illness, injury, and other physical and mental harms in people.
Healthcare sector is much diversified and is full of opportunities in every segment.

## Slide 10: Healthcare Application with IoT
Overview
Healthcare is delivered by health professionals.
  Medicine
  Dentistry
  Pharmacy
  Nursing
  Psychology
  And other health professions are all part of health care.
Healthcare has become one of India’s largest sector in terms of revenue and employment.

## Slide 11: Healthcare Application with IoT
Importance
Before Internet of Things, patients’ interactions with doctors were limited to visits.
There was no way doctors or hospitals could monitor patients’ health continuously.
IoT enabled devices have made remote monitoring in the healthcare sector possible.
IoT helps
  To keep patients safe and healthy,
  Empowering physicians to deliver superlative care.

## Slide 12: Healthcare Application with IoT
Importance
Remote monitoring of patient’s health helps in
  Reducing the length of hospital stay and
  Prevents re-admissions.
IoT has applications in healthcare that benefit to
  Patients
  Families
  Physicians
  Hospitals and
  Insurance companies.

## Slide 13: Healthcare Application with IoT
Requirements for IoT Setup
Sensors
  Heartbeat Sensor
  Oxygen Level Sensor
  Glucose Level Sensor
Controller
  ESP8266 Node MCU or
  Arduino Uno with Wi-Fi or Network Shield
For Fog Computing
  Raspberry Pi or
  PC
LAN and WAN Connectivity
  Router and Switches
  Wireless Access Point
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet

## Slide 14: Healthcare Application with IoT
Architecture
Heartbeat Sensor Node
Oxygen Sensor Node
Glucose Sensor Node
Patients Family
Cloud Services
Central and Remote
Storage/Analysis
Fog Computer
Within Organization for Local Analysis and Processing
Local Care Taker Monitoring
Nursing Staff and Doctors
Remote Care Taker Monitoring
Nursing Staff and Doctors
Data Analytics
Research / Decision Making
Controller Node
Patient Wise Node
Wi-Fi
Wi-Fi
Wi-Fi
Wi-Fi LAN
Internet Gateway
Internet
Internet
Internet
Wi-Fi / LAN

## Slide 15: Healthcare Application with IoT
How it works
All the sensor nodes should be placed on patient body, either direct or using wearables.
The sensor nodes should have Wi-Fi connectivity with a controller node of the patient.
The sensor nodes sends the sensed data to the controller node.
The controller node collects
  The data from all the sensors,
  Apply some business logic on it as per the requirements and
  Send it to Fog computer.
All the controller nodes of all the patients should have connected with the Fog computer network.

## Slide 16: Healthcare Application with IoT
How it works
Fog computer
  Receives all the data from all the controller nodes
  Execute some business logic and
  Do analysis on the collected data, and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the care taker team (nursing staff and doctors).
The Fog computer should have Internet connectivity for the cloud communication.
All the local care taker team members can be accessed health status of all the patients from the Fog computer.

## Slide 17: Healthcare Application with IoT
How it works
The cloud
  Stores all the data received from the Fog
  Execute some business logic
  Do analysis on the stored data
All those who have rights to access the cloud data can get health records of the patients, like
  Remote care taker team members
  Data analytics team
  Patient family members
The care taker and data analytics teams may execute corrective action based on the data and alert messages.

## Slide 18: Healthcare Application with IoT
Summery
IoT has changed people’s lives by enabling constant tracking of health conditions.
Wearables connected devices like blood pressure and heart rate monitoring cuffs, glucometer etc. give patients attention.
On any changes in the routine activities of a person, alert message sends to family members and health service providers.
IoT enables healthcare professionals to be more watchful.
Data collected from IoT devices can help physicians identify the best treatment process.
IoT devices tagged with sensors are used for tracking real time location of medical equipment like wheelchairs, nebulizers, oxygen pumps and other monitoring equipment.
IoT-enabled hygiene monitoring devices help in preventing patients from getting infected.
It also help in asset management like pharmacy inventory control, and environmental monitoring, for instance, checking refrigerator temperature.

## Slide 19: IoT Application in Retail
Retail is the process of selling consumer goods or services to end-users for earning a profit.
The retail sectors can be divided into
  Food,
  Clothing & Textiles,
  Consumer Durables,
  Footwear,
  Jewelry,
  Books-Music-Gift Articles, etc.
Overview

## Slide 20: IoT Application in Retail
Importance
In the retail industry customer plays key roll
The retail industry is rapidly transforming with IoT solutions.
IoT is taking the center stage in the sector.
Inventory management has been an expensive and tedious process.
IoT system automatically monitors inventory.
Send alert messages to managers if a certain item is running low or going to expire soon.
IoT devices are also helpful for avoiding
  Oversupply
  Shortage of goods and
  Thefts in stores.

## Slide 21: IoT Application in Retail
Importance
Customers are notified about discounts and offers in real-time.
It give data about customer behavior and routes.
IoT helps to increase
  Customer loyalty,
  Boost sales,
  Offer a personalized experience, and
  Improve inventory management.

## Slide 22: IoT Application in Retail
Controller
  ESP32 MCU or
  Arduino Uno with Wi-Fi or Network Shield
LAN and WAN Connectivity
  Router and Switches
  Wireless Access Point
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
  Alarm
  Water Sprinkler
  Beacons
  RFID Tag and RFID Reader
Sensors
Actuators and Tags
  Touch Sensors
  Gas Sensors
  Fire Sensors
  IR Sensors

## Slide 23: IoT Application in Retail
Architecture
Local Server
Within Organization for Local Analysis and Processing
Wi-Fi LAN
Cloud Services
Central
Storage/Analysis
Internet Gateway
Monitoring System
Store Manager and Other Staff
Internet
Data Analytics
Research / Decision Making
Internet
Customers
Internet
Wi-Fi / LAN
RFID Readers
On Smart Shelves
Controller Nodes
Wi-Fi
Wi-Fi
Wi-Fi
Touch Sensor Nodes
Gas & Fire Sensor Nodes
Light & Temp. Sensor Nodes
Camera & IR
Sensor Nodes
For Feedback
For
Safety
For
Ambiance
For In-Store,
Entry-Exit & Parking
Alarm & Water Sprinkler Node
Wi-Fi / LAN
For Safety
Beacons
For In-store Navigation &
Real Time Offers
Bluetooth
Beacon Data
RFID Tags
On Each Item
RIFD Tag Data
For Inventory Management

## Slide 24: IoT Application in Retail
How it works
All the sensor nodes and Beacons should be placed at various places in the store, washroom and parking area.
The sensor nodes should have Wi-Fi connectivity with controller nodes.
The sensor nodes sends the sensed data to the controller nodes.
The controller nodes
  Collects the data from all the sensors,
  Apply some business logic on it as per the requirements and
  Send it to local computer.

## Slide 25: IoT Application in Retail
How it works
RFID readers should be placed at items display shelves to detect item presence in the shelves for the stock management.
All the controller nodes and RFID readers should have connected with the Local Area Network.
RFID tags should be attached with each and every item which are likely to be monitored.
Using the RFID tags one can monitor location and stock of the item.
RFID tags is also useful for auto billing and queue less exit.

## Slide 26: IoT Application in Retail
How it works
Touch sensors are used for customers’ feedback about ambiance and cleanness at various places like washroom, trial room etc.
Light and Temperature sensors are used for ambiance monitoring which leads to energy saving and customer comfort.
Camera and IR sensors are placed for monitoring people density at various places, person in-out ratio for store and the parking area.
Gas sensors are used for monitoring various gases levels in the store.
Fire sensor are used for detecting fire in the store and send the alert signal to the Alarm & Water Sprinkler Node

## Slide 27: IoT Application in Retail
How it works
An alarm system and the water sprinkling system are used for fire safety, should have connected with a controller node
Local Server
  Receives all the data from all the controller nodes,
  Execute some business logic and
  Do analysis on the collected data, and
  Send the essential data to the cloud computer.
The server computer should have Internet connectivity for the cloud communication.
The cloud
  Stores all the data received from the local server,
  Execute some business logic and
  Do analysis on the stored data.

## Slide 28: IoT Application in Retail
How it works
All those who have rights to access the cloud data can get desire information and alerts, like
  Store manager
  Staff members
  Data analytics team
  customers
The store manager and data analytics teams may execute corrective action based on the data.

## Slide 29: IoT Application in Retail
How it works
Beacons, a Bluetooth Low Energy (BLE) device
  Automatically connect with customers’ smartphones when they entered in the coverage area.
  Send push notifications directly to the customers.
Beacons can be installed at various places
  For customer in-store navigation,
  To know foot fall in particular area of the store, and
  Collecting data about customer behavior and routes.
Customers are notified about discounts and offers in real-time using the beacons system.

## Slide 30: IoT Application in Retail
Summery
IoT will dramatically transform and innovate the retail industry in the coming years.
The integration of IoT solutions will enable retail companies,
  To create successful marketing campaigns based on customer behavior,
  Deliver high-quality services,
  Improve inventory management, and
  Reduce operational costs.

## Slide 31: Driver Assistance Application with IoT
Overview
Vehicle manufacturing companies are trying to make vehicles more comfortable and safe for their passengers.
They are experimenting to design a system that could monitor and alert the user suffering from highway hypnosis or white line fever.
As well as they need an IoT based system to prevent accidents caused by drowsy driver.

## Slide 32: Driver Assistance Application with IoT
Importance
Driver’s drowsiness is one of the major factor is reported in road accidents.
Drowsiness is a kind of sleeping sensation which can lead for closing eyes.
Drowsiness make one physically inactive and insensitive to surroundings.
So we need to monitor driver’s consciousness along with his acceleration pattern and steering angle.
If any deviation is detected, a system should be there to alert the driver.
A process of detecting the deviation and drowsiness of the driver should be developed.

## Slide 33: Driver Assistance Application with IoT
Importance
Using Image Processing and Machine Learning (ML) technology a system can be developed.
The system detect whether the driver has deviated or not, by monitoring the driver’s
  facial movements,
  Eye Aspects Ration (EAR) for drowsiness,
  acceleration pattern and
  change in the steering angle

## Slide 34: Driver Assistance Application with IoT
Requirements for IoT Setup
Sensors
  Ultrasonic Sensor
Cameras
On Board Diagnostic (OBD) Access
Controlling
  Raspberry Pi
WAN Connectivity
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet

## Slide 35: Driver Assistance Application with IoT
Architecture
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Data Analytics
Research / Decision Making
Internet
Vehicle Owner
Internet
Alert System
Driver
Wi-Fi / Bluetooth
Vehicle Computer
Within Vehicle for Local Analysis and Processing
USB
Internet
Wired / Bluetooth
Ultrasonic Sensor Nodes
Distance
Surrounding Vehicle
Bluetooth
Steering Angle
Speed
Variation
OBD
On Board Diagnostics Unit
Deviation Detection System
Lane Detection
EAR Value
Camera
Camera Units
Drowsiness Detection System
Facial Area

## Slide 36: Driver Assistance Application with IoT
How it works
Camera units should be placed on board for capture the face of driver and road view.
The camera units should have USB connectivity with vehicle computer.
The camera units sends the sensed data to the vehicle computer.
The ultrasonic sensor nodes should be placed at various place on outside the vehicle for detecting surrounding distance.
All the sensor nodes should have Wired / Bluetooth connectivity with the vehicle computer.

## Slide 37: Driver Assistance Application with IoT
How it works
The OBD unit of the vehicle should have Bluetooth connectivity with the vehicle computer
The vehicle computer
  Collects the data from the camera units, OBD unit and the sensor nodes, and
  Apply some business logic,
  Do analysis on the collected data on it as per the requirements and
  Send the filtered limited data to the cloud computer as well as
  Send the alert messages to the driver.
The vehicle computer should have Internet connectivity for the cloud communication.

## Slide 38: Driver Assistance Application with IoT
How it works
The driver side camera capture the drive facial and eye movement.
The camera send the captured images to vehicle computer for EAR value and other calculation.
EAR (Eye Aspect Ratio) is measured using following equation.
  Where
    is distance between points P2 and P6
    is distance between points P3 and P5
    is distance between points P1 and P4
Using image processing the system finds the eye positions and calculate the above mentioned distance of the six points.
When the driver closes his eye, the EAR value eventually drops to zero and the system detects drowsiness of the driver.

## Slide 39: Driver Assistance Application with IoT
How it works
The road side camera capture the front view images.
The capture images sends to the vehicle computer for
  Detecting lane
  Objects
  Sign boards
Deviation is monitored using OBD (On-Board Diagnostics) device.

## Slide 40: Driver Assistance Application with IoT
How it works
OBD can record the pattern of acceleration and steering angles during the drowsiness of the driver.
Compare the recorded values with the threshold value and the historical data for the actual deviation.
All the calculated data is sent to the data analytics and obtained result, is used to alert the driver.
The cloud data also useful for the vehicle owner.

## Slide 41: Collision Impact Detection Using IoT
Overview
Modern vehicles are equipped with the collision detection mechanism.
It blow up airbags when an accident occurs and save lives in major cases.
But if the collision is massive then the airbags may not sufficient.
In these cases emergency help needed to save the lives.
So we need a system that measure the severity impact of the collision and send alert messages.

## Slide 42: Collision Impact Detection Using IoT
Overview
The messages contents
  Location of the accident
  Severity impact,
  Fire status,
  Speed of the vehicle,
  Number of passengers,
  Time of the incident, etc.
Broadcast the messages to all the authorities like
  Ambulance service,
  Hospitals,
  Highway patrolling team,
  Fire brigade,
  Police,
  Family member of the vehicle owner, etc.

## Slide 43: Collision Impact Detection Using IoT
Importance
If a single accident occur in along highway then it can be managed without the data of severity of the collision.
When multiple accident occurs on the highway then the severity data is very important to save lives of the very serious victims.
Based on the data and severity impact, all the emergency help will be reached timely at the point.
Thus, we need an IoT based system that sense the necessary parameters of the collision.

## Slide 44: Collision Impact Detection Using IoT
Requirements for IoT Setup
Sensors
  FSR Sensor
  Fire Sensor
  GPS Sensor
Cameras
OBD Access
Controlling
  Raspberry Pi
WAN Connectivity
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet

## Slide 45: Collision Impact Detection Using IoT
Architecture
Cloud Services
Central and Remote
Storage/Analysis
Internet Gateway
Data Analytics
Research / Decision Making
Internet
Vehicle Owner
Family
Internet
Vehicle Computer
Within Vehicle for Local Analysis and Processing
Wired / Bluetooth
FSR
Sensor Nodes
Severity Impact
Bluetooth
Speed
OBD
On Board Diagnostics Unit
For Speed
USB
Camera
Camera Units
For Passenger Counting
Passenger Count
Emergency Help
Service Provider
Internet
Ambulance
Hospitals
Highway Patrolling
Fire Brigade
Police
GPS
Node
For Location
Wired / Bluetooth
Fire
Sensor
Node
For Detecting Fire
Wired / Bluetooth

## Slide 46: Collision Impact Detection Using IoT
How it works
Force sensitive resistor (FSR) sensors are useful to measure pressure applied on the vehicle during the collision.
The FSR sensor are mounted on the vehicle at the places where impact probability is higher than the other part of vehicle during an accident.
Based on the FSR data we can estimate the severity of the collision.
Fire sensor and GPS should be placed at appropriate place of the vehicle.
All the sensor nodes should have Wired / Bluetooth connectivity with the vehicle computer.
Camera units should be placed on board for capturing all the passengers.

## Slide 47: Collision Impact Detection Using IoT
How it works
The camera units should have USB connectivity with vehicle computer.
The camera units sends the captured images to the vehicle computer.
The OBD unit of the vehicle should have Bluetooth connectivity with the vehicle computer
The vehicle computer
  Collects the data from the camera units, OBD unit and the sensor nodes.
  Apply some business logic,
  Do analysis on the collected data on it as per the requirements.
  Send the analyzed data to the cloud computer.
  Should have Internet connectivity

## Slide 48: Collision Impact Detection Using IoT
How it works
Using OBD (On-Board Diagnostics) device the system records speeds of the vehicle.
The fire sensor and GPS also sends the sensed data to the vehicle computer.
Based on the analyzed data and severity of the collision the cloud system sent alert messages to all the emergency help service provider and family member of the vehicle owner.
The cloud data is used for data analytics and to provide the priority based emergency services.
The system is automatic activated when the collision is detected.

## Slide 49: Water Quality Monitoring - IoT Based Application
Overview
Water is essential for life and the polluted water is a one of the major challenge in the world.
So water quality monitoring is necessary for us.
Water Quality Monitoring (WQM) helps in preventing and controlling water pollutions.
Water quality should be checked regularly to avoid serious health issues.
IoT can help to develop a perfect WQM system.

## Slide 50: Water Quality Monitoring - IoT Based Application
At present water quality is monitored very expensive and inefficient by manual or nodal network methods.
Manual Method
  Water samples are taken manually from the different points of a water area.
  The samples sent to laboratories
  Various tests are conducted to find the values of
    PH, Conductivity and Temperature
    TDS, Dissolved Oxygen
    Turbidity
    Chloride Content
  The reports of the test sends to the concern authorities with in a week.
Importance

## Slide 51: Water Quality Monitoring - IoT Based Application
Importance
Manual Method
The methods have some limitations like
  Chance of human error in the sampling
  Sampling cost is very high because of to cover very large area of waterbody
  Sampling and Testing both are time consuming
  Not real-time monitoring which leads to may serious issues.

## Slide 52: Water Quality Monitoring - IoT Based Application
Nodal Network Method (Electronics Sensor Monitoring)
  Water quality is measured by electronic sensors installed in the different points of a water area.
  All the sensors are wirelessly connected with the Internet.
  The water quality data sends to the cloud server at regular interval.
  This method is giving real-time data contras to the manual method.
  System architecture of the monitoring system is divided into following four areas
    Sensing
    Data Collection
    Processing
    Communication
Importance

## Slide 53: Water Quality Monitoring - IoT Based Application
Nodal Network Method (Electronics Sensor Monitoring)
The methods have following limitations
  Very expansive
  Maintenance of the sensors along with power source are challenging
  Natural disaster and aquatic animal movement in the waterbody may damage the sensors
  The sensors are not moveable
Importance

## Slide 54: Water Quality Monitoring - IoT Based Application
Importance
A low cost solution is possible for WQM using latest technology, Data Analytics, USVs, Machine Learning, AI and IoT.
No need to install sensors permanently into the waterbody in the solution
An autonomous boat (USV), mounted with all the necessary sensors can
  Collect the water quality data and
  Send the data to the cloud for data analytics
All the necessary parameters of water can be tracked and measured.
Detailed report of the containment status of the entire waterbody can be generated.

## Slide 55: Water Quality Monitoring - IoT Based Application
Controller
  ESP32 MCU or
  Arduino Uno with Wi-Fi or Network Shield
WAN Connectivity
  GPRS or GSM Module
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
Water Sensors Kit
  PH Sensor
  GPS Sensor
  Turbidity Sensor
  TDS and Dissolved Oxygen Sensor
  Temperature Sensor
  Conductivity Sensor
Unmanned Surface Vehicle (USV)

## Slide 56: Water Quality Monitoring - IoT Based Application
Architecture
Cloud Services
Central and Remote
Storage/Analysis
Internet
Data Analytics
Research / Decision Making
Internet
Pollution Control Board
Internet
Report Generation
USV Controller Node
Unmanned Surface Vehicle
Wired
Water Quality Sensors Kit
GPS Sensor
Turbidity Sensor
TDS and DO Sensor
PH
Sensor
Temperature Sensor
Conductivity Sensor
Sensors Kit Controller
Node
GPRS / GSM Module
Wired
USV
Control Panel
Internet
Base Station,
USV Operator

## Slide 57: Water Quality Monitoring - IoT Based Application
How it works
A bundle of all the sensors or a water quality sensor kit should be mounted on an autonomous or unmanned surface vehicle (USV).
The USV can be operated by an embedded controller node.
The USV should have GSM or GPRS internet connectivity with the cloud server.
The sensor kit sense the following values
  PH Value of Water - PH Sensor
  Temperature of Water - Temperature Sensor
  Conductivity of Water - Conductivity Sensor
  Clarity of Water - Turbidity Sensor
  Dissolved Solid and Oxygen in Water– TDS and DO Sensor
  Location of the reading - GPS Sensor

## Slide 58: Water Quality Monitoring - IoT Based Application
How it works
The kit controller node sends all the sensed data to the cloud server via GPRS/GSM module
The GPRS/GSM module is used to provide the Internet connectivity with the cloud server.
The cloud
  stores all the data received from the USVs,
  Execute some business logic and
  Do analysis on the stored data.
All those who have rights to access the cloud data can get water quality records of the waterbody.
Like,
  Members of Pollution Control Board
  Data analytics team
  USV operator

## Slide 59: Water Quality Monitoring - IoT Based Application
How it works
Authorities of the board and data analytics teams may execute corrective action based on the data.
An USV control panel is installed in the base station of the WQM system.
The control panel should have internet connectivity for controlling the USV.
Using the control panel, an operator can set paths and control the USV.

## Slide 60: Smart Lavatory - IoT Based Application
Overview
In the all businesses retaining old customer is more meaningful then the finding new.
It is possible by
  Offering good quality products,
  Best services and
  The pleasant experience while visiting your place.
Hygiene and comfort in lavatory is one of the major concern of the businesses.
Maintaining and monitoring cleanliness in lavatory is a challenging task.

## Slide 61: Smart Lavatory - IoT Based Application
Importance
Mostly lavatory cleaning and monitoring is manually done by cleaning staff.
Because of the manual process some time it’s not done properly.
Unclean lavatory may become a root cause of many diseases.
User may suffer because of unavailability of water or toilet papers in many cases.
Slippery and wet floor might be unsafe for users.
An IoT based smart lavatory monitoring system is needed to solve the above mentioned issues.

## Slide 62: Smart Lavatory - IoT Based Application
Controller
  ESP32 MCU or
  Arduino Uno with Wi-Fi or Network Shield
LAN and WAN Connectivity
  Router and Switches
  Wireless Access Point
Cloud Services
For Monitoring and Analysis
  PC
  Mobile
  Tablet
Requirements for IoT Setup
Water Sensors Kit
  MQ05 Gas Sensor
  Touch Sensor
  Sharp IR Sensor
  Water Level Float Sensor

## Slide 63: Smart Lavatory - IoT Based Application
Architecture
Local Server
Within Organization for Local Analysis and Processing
Wi-Fi LAN
Cloud Services
Central
Storage/Analysis
Internet Gateway
Monitoring System
Store Manager,
Support Agency and Other Staff
Internet
Data Analytics
Research / Decision Making
Internet
Customers
Internet
Wi-Fi / LAN
Cleaning & Monitoring Team
Sweepers and
Supervisor
Controller Nodes
Wi-Fi
Wi-Fi
Wi-Fi
Touch Sensor Nodes
Gas
Sensor Nodes
Water Level Float Sensor Nodes
Sharp IR
Sensor Nodes
For Feedback
For
Hygiene
For
Flush Tank
For Toilet Paper Dispenser

## Slide 64: Smart Lavatory - IoT Based Application
How it works
All the sensor nodes should be placed at various places in the lavatory area.
The sensor nodes should have Wi-Fi connectivity with controller nodes.
The sensor nodes sends the sensed data to the controller nodes.
The controller nodes
  Collects the data from all the sensors,
  Apply some business logic on it as per requirements and
  Send it to local computer.
All the controller nodes should have connected with the Local Area Network.

## Slide 65: Smart Lavatory - IoT Based Application
How it works
Gas sensors are used for monitoring various gases levels like ammonia and methane level in the lavatory.
Touch sensors are used for customers’ feedback about ambiance and cleanness in the lavatory.
Water level float sensors are used for monitoring water level in the flush tank and the flush count.
Sharp IR sensors are placed in the toilet paper dispenser for monitoring remaining toilet papers.

## Slide 66: Smart Lavatory - IoT Based Application
How it works
Local server
  Receives all the data from all the controller nodes,
  Execute some business logic and
  Do analysis on the collected data, and
  Send the essential data to the cloud computer.
All the cleaning & monitoring team members can be accessed following from the local server .
  Status of lavatory cleanness,
  Water and toilet paper availability
The local server should have Internet connectivity to communicate with the cloud.

## Slide 67: Smart Lavatory - IoT Based Application
How it works
The cloud
  stores all the data received from the local server,
  execute some business logic and
  do analysis on the stored data.
All those who have rights to access the cloud data can get desire information and alerts, like
  Store manager
  Service support agency
  Local staff members
  Data analytics team
  Customers
The store manager and data analytics teams may execute corrective action based on the analyzed data.